Product List

(all products are based on micro-optic filter technology)

Polarization Maintaining (PM) Fiber-Optic Products:

- Polarization Maintaining Couplers (all ports PM) - PMC

- 1x2 PM Couplers (inline package, any split ratio)

- 2x2 PM couplers

- 1x4 PM Couplers

- 1x8 PM Couplers

- Polarization Maintaining Taps (Tap port SM) - PMTAP

- Polarization Maintaining WDM - PMWDM

- 1480/1550

- 980/1550

- 1300/1550 (all ports are PM)

- 980/1064, 980/1050, 980/1040, 980/1030, 980/ ( can be customized to customer need)

- Other combinations available

- Polarization Maintaining Isolators - SPFI and PMFI

- Polarization Maintaining (Single Polarization) Isolators (Single Stage) - SPFI-SS

- Polarization Maintaining (Single Polarization) Isolators (Double Stage) - SPFI-DS

- Polarization Maintaining (true PM isolators transmitting and isolating 2 orthogonal polarizations simultaneously) - PMFI

- Integrated Polarization Maintaining Tap/SP Isolator (any tap ratio) - PMTAP-SPFI/SS

- Integrated Polarization Maintaining WDM/SP Isolator (WDM can be 980/1550, 1480/1550) - PMWDM-SPFI/SS

- Polarization Maintaining Fiber Circulator - PMFC

- Polarization Combiner/Splitter (inline package) - PDM

- 1550nm

- 1480nm

- 1060nm

- 980nm

- Fiber Optic Polarizers - FOP

- Polarization Maintaining Jumpers (PM Patchcord) - PMJ

- Polarization Maintaining Connectorization - PM Connectors

- Polarization Maintaining Faraday Rotator PMFR

- Other Specialty Polarization Maintaining Products

Polarization Insensitive Fiber-Optic Products:

- Polarization Insensitive Couplers (any split ratio) - PIC

- Polarization Insensitive Taps (any tap ratio) - PITAP

- Polarization Insensitive WDM (980/1550, 1480/1550, 1300/1550, 980/1064, 980/1050, 980/1040, 980/1030) - PIWDM

- Polarization Insensitive Isolators (1550) - PIFI

- Faraday Rotator Mirror - FRM

- Other Specialty Polarization Insensitive Products

1x2 Polarization Maintaining (PM) Coupler (PMC-1x2)

| Description: The polarization maintaining (PM) coupler is a compact low loss micro-optic filter type inline PM coupler (1x2) which provides PM optical signal splitting (various splitting ratios available) over a wide bandwidth while preserving the polarization with high extinction ratio. It can also be provided with a PM isolator integrated in the same package. |  |  |
| --- | --- | --- |
| Applications: EDFA Communications CATV Instrumentation Sensor systems Multiple channel splitting |  | Key Features: Wavelength flat operation Low insertion loss High polarization extinction ratio High uniformity High return loss High stability and reliability Compact inline package, 5.5mm OD |

Specifications:

| Wavelength | 532, 680, 830, 980, 1060, 1125, 1310, 1480, 1550, 1620nm (± 20nm) Other wavelengths available |
| --- | --- |
| Split Ratio | Standard: 50/50, 30/70, 20/80, 10/90, 5/95, 2/98, 1/99 (any split ratio from 0.1/99.9 to 50/50 is available) |
| Excess Loss (excluding splitting) | (0.8dB (typical <0.5dB) |
| Split Uniformity | (0.5dB (typical <0.3dB) |
| Polarization Extinction Ratio (w/o connectors) | ( 20dB (typical >25dB) |
| Return Loss | ( 50dB |
| Optical Power | 300mW |
| Fiber | PM fiber, all ports |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

| PMC-IL-1x2 |  |  |  |  | I | O |  | I | O |  | I | O |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Split Ratio |  | PM Fiber |  |  | Fiber Length |  |  | Connectors |  |  |
| 1550 | =1 | 50/50 | =1 | Bowtie | =1 | =1 | 1m | =1 | =1 | None | =0 | =0 |
| 1310 | =2 | Other | =2 | Panda | =2 | =2 | Other | =2 | =2 | FC/PC | =1 | =1 |
| Other | =3 |  |  | Other | =3 | =3 |  |  |  | FC/APC | =2 | =2 |
|  |  |  |  |  |  |  |  |  |  | Other | =3 | =3 |

2x2 Polarization Maintaining (PM) Coupler (PMC-2x2)

| Description: The 2x2 polarization maintaining (PM) coupler is a low loss micro-optic filter type coupler (2x2) which provides PM optical signal coupling/splitting over a wide bandwidth while preserving the polarization with high extinction ratio in a rugged package. It utilizes advanced micro-optic filter technology to achieve high polarization maintaining coupler performance. |  |  |
| --- | --- | --- |
| Applications: PM-EDFA Communications CATV Instrumentation Sensor systems |  | Key Features: Wavelength flat operation Low insertion loss High polarization extinction ratio High uniformity High return loss High stability and reliability Rugged package |

Specifications:

| Split Configuration | 2x2 |
| --- | --- |
| Wavelength | 532, 680, 830, 980, 1060, 1125, 1310, 1480, 1550, 1620nm (± 20nm) Other wavelengths available |
| Excess Loss (maximum) | (1.5dB (typ <1dB) |
| Insertion Loss (maximum) | (4.5dB (typ <4dB) |
| Uniformity | (0.5dB |
| Polarization Extinction Ratio | ( 20dB |
| Return Loss | (50dB |
| Directivity | (50dB |
| Optical Power | 300mW |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Fiber Type | PM fiber on all ports (Panda, Bowtie, etc.) |
| Package | Rugged package, H=20mm, W=55mm, L=120mm |

Ordering Information:

| PMC-2x2 |  |  |  |  |  |  |  |  |  |  | In | Out |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Configuration |  | PM Fiber |  | Length |  | Cable |  | Connectors |  |  |
| 1550 | =1 | 2x2 | =2 | Bowtie | =1 | 1m | =1 | None | =0 | None | =0 | =0 |
| Other | =2 |  |  | Panda | =2 | Other | =2 | 3mm | =1 | FC/PC | =1 | =1 |
|  |  |  |  | Other | =3 |  |  | 900m | =2 | FC/APC | =2 | =2 |
|  |  |  |  |  |  |  |  | Other | =3 | Other | =3 | =3 |

1xN Polarization Maintaining Coupler (PMC-1xN)

| Description: The 1xN polarization maintaining (PM) coupler is a low loss micro-optic filter type coupler (1xN) which provides PM optical signal combining or splitting over a wide bandwidth while preserving the polarization with high extinction ratio in a rugged package. It utilizes advanced micro-optic filter technology to achieve high polarization maintaining coupler performance. |  |  |
| --- | --- | --- |
| Applications: EDFA Communications CATV Instrumentation Sensor systems Multiple channel splitting |  | Key Features: Wavelength flat operation Low insertion loss High polarization extinction ratio High uniformity High return loss High stability and reliability Rugged package |

Specifications:

| Split Configuration | 1x2 | 1x4 | 1x8 |
| --- | --- | --- | --- |
| Wavelength | 532, 680, 830, 980, 1060, 1125, 1310, 1480, 1550, 1620nm (± 20nm) Other wavelengths available |
| Excess Loss (maximum) | (0.8dB | (2.0dB | (2.0dB |
| Excess Loss (typical) | <0.5dB | <1.0dB | <1.5dB |
| Insertion Loss (maximum) | (3.8dB | (8.0dB | (11.0dB |
| Insertion Loss (typical) | <3.5 dB | <7.0dB | <10.5dB |
| Uniformity | (0.6dB | (0.8dB | (1.0dB |
| Polarization Extinction Ratio (Higher extinction ratio available upon request) | ( 20dB | ( 20dB | ( 20dB |
| Return Loss | (50dB | (50dB | (50dB |
| Directivity | (50dB | (50dB | (50dB |
| Optical Power | 300mW |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Fiber Type | PM fiber on all ports (Panda, Bowtie, etc.) |
| Size | Inline OD=5.5mm | H=20mm, W=55mm, L=120mm | H=24mm, W=80mm, L=120mm |

Ordering Information:

| PMC-1xN |  |  |  |  |  |  |  |  |  |  | In | Out |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Configuration |  | PM Fiber |  | Length |  | Cable |  | Connectors |  |  |
| 1550 | =1 | 1x2 | =2 | Bowtie | =1 | 1m | =1 | None | =0 | None | =0 | =0 |
| 1310 | =2 | 1x4 | =4 | Panda | =2 | Other | =2 | 3mm | =1 | FC/PC | =1 | =1 |
| Other | =3 | 1x8 | =8 | Other | =3 |  |  | 900m | =2 | FC/APC | =2 | =2 |
|  |  | Other | =xx |  |  |  |  | Other | =3 | Other | =3 | =3 |

1x2 Polarization Insensitive Fiber Optic Coupler (PIC-1x2)

| Description: The polarization insensitive fiber optic coupler is a compact low loss micro-optic filter type 3 port (1x2) coupler which provides accurate optical signal split over a wide bandwidth. It features low insertion loss, low PDL, flat performance over a wide bandwidth, and high return loss in a compact inline package. |  |  |
| --- | --- | --- |
| Applications: EDFA Communications CATV Instrumentation Sensor systems |  | Key Features: Wavelength flat wideband operation Low insertion loss Low PDL High return loss High stability and reliability Compact inline package, 5.5mm OD |

Specifications:

|  | Premium Grade | Grade A |
| --- | --- | --- |
| Signal Wavelength | 532, 680, 830, 980, 1060, 1125, 1310, 1480, 1550, 1620nm (± 20nm) Other wavelengths available |
| Coupling Ratio | Standard: 50/50, 30/70, 20/80, 10/90, 5/95, 2/98, 1/99 (any split ratio from 0.1/99.9 to 50/50 is available) |
| Insertion Loss (for 50/50 split) | (3.6dB Max (<3.5dB typical) | (3.8dB Max (<3.6dB typical) |
| Uniformity (for 50/50 split) | (0.5dB | (0.8dB |
| Polarization Dependent Loss (PDL) | ( 0.05dB (typ <0.02dB) | ( 0.1dB (typ <0.05dB) |
| Return Loss | ( 50dB (typ >55dB) | ( 50dB |
| Optical Power | 300mW |
| Fiber | SMF28 |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

| PIC-1x2 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Grade |  | Split Ratio |  | Fiber Type |  | Connectors |  |
| 1550 | =1 | Premium | =P | 50/50 | =1 | SMF28 (250) | =1 | None | =0 |
| 1310 | =2 | Grade A | =A | Other | =2 | Other | =2 | FC/PC | =1 |
| Other | =3 |  |  |  |  |  |  | FC/APC | =2 |
|  |  |  |  |  |  |  |  | Other | =3 |

Polarization Maintaining Tap Coupler (PMTAP)

| Description: The polarization maintaining (PM) tap coupler is a compact low loss micro-optic filter type inline coupler (1x2) which provides a signal tap for monitoring over a wide bandwidth while preserving the transmitted polarization with high extinction ratio. It utilizes advanced filter technology to yield high extinction ratio, low insertion loss, wide bandwidth and high return loss in a compact package. The tap coupler can be provided with a wide range of tap ratios. It can also be provided with a PM isolator integrated in the same package. |  |  |
| --- | --- | --- |
| Applications: EDFA Communications CATV Instrumentation Sensor systems |  | Key Features: Wavelength flat operation Low insertion loss High polarization extinction ratio High return loss High stability and reliability Compact inline package, 5.5mm OD |

Specifications:

|  | Premium Grade | A Grade |
| --- | --- | --- |
| Signal Wavelength | 830, 980, 1060, 1125, 1310, 1480, 1550, 1620nm (± 20nm) Other wavelengths available |
| Tap Ratio | Any split ratio from 0.1/99.9 to 50/50 |
| Excess Loss (excluding splitting) | (0.7dB (0.5dB Typ) | (0.9dB (<0.7dB Typ) |
| Polarization Extinction Ratio | ( 20dB (typ (25dB) | ( 20dB (typ (22dB) |
| Return Loss | ( 55dB | ( 50dB |
| Optical Power | 300mW |
| Fiber | PM fiber input and output (customer may specify type), SMF28 (250) on tap port |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

| PMTAP |  |  |  |  |  |  |  |  |  |  | I | O | Tap |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Grade |  | Tap |  | Signal Fiber |  | Tap Fiber |  | Connectors |  |  |  |
| 1550 | =1 | Premium | =P | 10% | =1 | Bowtie | =1 | SMF28 | =1 | None | =0 | =0 | =0 |
| 1310 | =2 | Grade A | =A | 5% | =2 | Panda | =2 | Other | =2 | FC/PC | =1 | =1 | =1 |
| Other | =3 |  |  | 1% | =4 | Other | =3 |  |  | FC/APC | =2 | =2 | =2 |
|  |  |  |  | Other | =5 |  |  |  |  | Other | =3 | =3 | =3 |

Polarization Insensitive Tap Coupler (PITAP)

| Description: The polarization insensitive tap coupler is a compact low loss micro-optic coupler which provides a signal tap for monitoring over a wide bandwidth. It utilizes advanced filter technology to achieve low insertion loss, wide bandwidth and high return loss in a compact package. The tap coupler can be provided with a wide range of tap ratios. |  |  |
| --- | --- | --- |
| Applications: EDFA Communications CATV Instrumentation Sensor systems |  | Key Features: Wavelength flat wideband operation Low insertion loss Low PDL High return loss High stability and reliability Compact inline package, 5.5mm OD |

Specifications:

| Signal Wavelength | 830, 980, 1060, 1125, 1310, 1480, 1550, 1620nm (± 20nm) Other wavelengths available |
| --- | --- |
| Tap Ratio | Any split ratio from 0.1/99.9 to 20/80 Other Ratios Available |
| Insertion Loss (Signal Path) | 0.4dB Typical, 0.6dB Max |
| Insertion Loss (Tap Path) | 0.4dB Typical, 0.6dB Max |
| Return Loss | ( 60dB |
| PDL | ( 0.05dB |
| Optical Power | 300mW |
| Fiber | SMF28 |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

| PITAP |  |  |  |  |  |  |  |  | I | O | Tap |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Tap % |  | Signal Fiber |  | Tap Fiber |  | Connectors |  |  |  |
| 1550 | =1 | 10% | =1 | SMF28 | =1 | SMF28 | =1 | None | =0 | =0 | =0 |
| 1310 | =2 | 5% | =2 | Other | =2 | Other | =2 | FC/PC | =1 | =1 | =1 |
| Other | =3 | 1% | =4 |  |  |  |  | FC/APC | =2 | =2 | =2 |
|  |  | Other | =5 |  |  |  |  | Other | =3 | =3 | =3 |

Integrated Polarization Maintaining Fiber-Optic Tap/Isolator (PMTAP-SPFI/SS)

| Description: The polarization maintaining (PM) fiber-optic tap/isolator combines the functionality of a PM isolator with a PM tap in one compact inline package thus providing significant advantages in performance, size, and cost. This hybrid product features high isolation, low insertion loss, high polarization extinction ratio, high return loss, and high thermal stability in a compact design. A wide range of tap ratios are available. |  |  |
| --- | --- | --- |
| Applications: EDFA (PM) CATV fiber optic systems External modulator transmitters Fiber lasers Fiber sensors |  | Key Features: High isolation Low loss High thermal stability High extinction High return loss Compact inline package, 5.5mm OD |

Specifications:

|  | Premium Grade | A Grade |
| --- | --- | --- |
| Center Wavelength (c) | 1550nm, 1480nm, 1300nm |
| Tap Split Ratio | Any split ratio from 0.1/99.9 to 20/80 Other Ratios Available |
| Tap Split Ratio Tolerance | (20% of specified tap ratio (example for 1% tolerance is (0.2% or 0.8-1.2%) |
| Peak Isolation (c, 23°C) | ( 38dB (typ >40dB) | ( 37dB (typ >38dB) |
| Isolation Over Wavelength (c±15nm, 23°C) | ( 32dB | ( 30dB |
| Excess Loss (c±20nm) excluding power in tap | ( 0.90dB (typ <0.5dB) | ( 1.1dB (typ <0.6dB) |
| Output Extinction Ratio | ( 22dB (typ >25dB) | ( 20dB (typ >22dB) |
| Return Loss (Input/Output) | ( 55/55dB | ( 50/50dB |
| Optical Power | 300mW |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Fiber Type | PM fiber on signal input and output ports, SMF fiber on tap port |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

| PMTAP-SPFI/SS |  |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Grade |  | Tap % |  | PM Fiber |  | SM Fiber |  | Length |  | Connectors |  |
| 1550 | =1 | Premium | =P | 10% | =1 | Bowtie | =1 | SMF28 | =1 | 1m | =1 | None | =0 |
| 1310 | =2 | Grade A | =A | 5% | =2 | Panda | =2 | Other | =2 | Other | =2 | FC/PC | =1 |
| Other | =3 |  |  | 1% | =4 | Other | =3 |  |  |  |  | FC/APC | =2 |
|  |  |  |  | Other | =5 |  |  |  |  |  |  | Other | =3 |

Polarization Maintaining (Single Polarization) Fiber Isolator - Single Stage (SPFI-SS)

| Description: The polarization maintaining (single polarization) fiber isolator eliminates back reflection and back scattering of optical signals in the transmitted polarization and maintains the polarization of the input light at high extinction. This single stage (SS) isolator features high isolation, very low insertion loss, high extinction ratio, high return loss, and very high thermal stability in a compact design. |  |  |
| --- | --- | --- |
| Applications: EDFA (PM) CATV fiber optic systems External modulator transmitters Fiber lasers Fiber gyros |  | Key Features: High isolation Very low loss Very high thermal stability High extinction High return loss Compact inline package, 5.5mm OD |

Specifications:

|  |  | Premium | A Grade |
| --- | --- | --- | --- |
| Center Wavelength (c) |  | 1310, 1480, 1550nm |
| Peak Isolation (c, 23°C) | Typ. | ( 45dB | ( 40dB |
| Isolation (c, 23°C) | Min. | ( 38dB | ( 37dB |
| Minimum Isolation (c±15nm, 23°C) | Min. | ( 32dB | ( 30dB |
| Insertion Loss (c±20nm, 23°C) | Typ. | ( 0.5dB | ( 0.5dB |
| Insertion Loss (c±20nm, 0 to 70°C) | Max. | ( 0.65dB | ( 0.8dB |
| Extinction Ratio (PM fiber output) | Min. | ( 22dB | ( 20dB |
| Extinction Ratio (PM fiber output) | Typ. | ( 25dB | ( 25dB |
| Return Loss (Input/Output) | Min. | ( 60/60dB | ( 60/55dB |
| Optical Power |  | 300mW |
| Operating Temperature |  | 0 to 70°C |
| Storage Temperature |  | -40 to 85°C |
| Size |  | Compact inline package, 5.5mm OD |

Ordering Information:

|  |  |  |  |  | I | O |  | I | O |  | I | O |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SPFI-SS |  |  |  |  |  |  |  |  |  |  |  |  |
| Wavelength |  | Grade |  | PM Fiber |  |  | Fiber Length |  |  | Connectors |  |  |
| 1550 | =1 | Premium | =P | Bowtie | =1 | =1 | 1m | =1 | =1 | None | =0 | =0 |
| 1310 | =2 | Grade A | =A | Panda | =2 | =2 | Other | =2 | =2 | FC/PC | =1 | =1 |
| Other | =3 |  |  | Other | =3 | =3 |  |  |  | FC/APC | =2 | =2 |
|  |  |  |  |  |  |  |  |  |  | Other | =3 | =3 |

Polarization Maintaining (Single Polarization) Fiber Isolator - Double Stage (SPFI-DS)

| Description: The polarization maintaining (single polarization) fiber isolator eliminates back reflection and back scattering of optical signals in the transmitted polarization and maintains the polarization of the input light at high extinction. This double stage (DS) isolator features very high isolation, very low insertion loss, high extinction ratio, high return loss, and very high thermal stability in a compact design. |  |  |
| --- | --- | --- |
| Applications: EDFA (PM) CATV fiber optic systems External modulator transmitters Fiber lasers Fiber gyros |  | Key Features: Very high isolation Very low loss Very high thermal stability High extinction High return loss Compact inline package, 5.5mm OD |

Specifications:

|  |  | Premium | A grade |
| --- | --- | --- | --- |
| Center Wavelength (c) |  | 1310, 1480, 1550nm |
| Peak Isolation (c, 23°C) | Typ. | ( 60dB | ( 55dB |
| Peak Isolation (c, 23°C) | Min. | ( 55dB | ( 50dB |
| Minimum Isolation (c±20nm, 23°C) | Min. | ( 50dB | ( 45dB |
| Insertion Loss (c±20nm, 23°C) | Typ. | ( 0.6dB | ( 0.8dB |
| Insertion Loss (c±20nm, 0 to 70°C) | Max. | ( 0.9dB | ( 1.1dB |
| Extinction Ratio (PM fiber output) | Min. | ( 22dB | ( 20dB |
| Extinction Ratio (PM fiber output) | Typ. | ( 25dB | ( 25dB |
| Return Loss (Input/Output) | Min. | ( 60/60dB | ( 60/55dB |
| Optical Power |  | 300mW |
| Operating Temperature |  | 0 to 70°C |
| Storage Temperature |  | -40 to 85°C |
| Size |  | Compact inline package, 5.5mm OD |

Ordering Information:

|  |  |  |  |  | I | O |  | I | O |  | I | O |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SPFI-DS |  |  |  |  |  |  |  |  |  |  |  |  |
| Wavelength |  | Grade |  | PM Fiber |  |  | Fiber Length |  |  | Connectors |  |  |
| 1550 | =1 | Premium | =P | Bowtie | =1 | =1 | 1m | =1 | =1 | None | =0 | =0 |
| 1310 | =2 | Grade A | =A | Panda | =2 | =2 | Other | =2 | =2 | FC/PC | =1 | =1 |
| Other | =3 |  |  | Other | =3 | =3 |  |  |  | FC/APC | =2 | =2 |
|  |  |  |  |  |  |  |  |  |  | Other | =3 | =3 |

Polarization Maintaining (Two Polarizations) Fiber Isolator (PMFI)

| Description: The polarization maintaining (PM) fiber isolator (PMFI) is a true PM isolator. It simultaneously transmits two orthogonal polarizations and eliminates the back reflection and back scattering in the two orthogonal polarizations simultaneously (i.e. it is a true PM isolator as compared to single polarization isolators). It maintains the polarization of the input light with high extinction ration in both polarizations. It features low insertion loss, high isolation, high extinction ratio, high return loss, and high stability in a compact design. |  |  |
| --- | --- | --- |
| Applications: External modulator transmitters Fiber amplifiers Fiber lasers Telecom and CATV fiber optic systems Fiber-optic sensors |  | Key Features: High isolation Low loss High thermal stability High extinction High return loss Compact inline package, 5.5mm OD |

Specifications:

|  | Premium | Grade A |
| --- | --- | --- |
| Center Wavelength (c) | 1550nm (other wavelengths available) |
| Peak Isolation (c, 23°C) | ( 40dB | ( 38dB |
| Minimum Isolation (c±15nm, 23°C) | ( 32dB | ( 30dB |
| Insertion Loss Typical (c±20nm, 23°C) | ( 0.5dB | ( 0.6dB |
| Insertion Loss Max (c±20nm, 0 to 70°C) | ( 0.8dB | ( 1.0dB |
| PDL Between Two Major Axis | (0.1dB | (0.15dB |
| Return Loss (Input/Output) | ( 60/60dB | ( 55/55dB |
| Extinction Ratio (PM fiber output, slow and fast axis) | ( 22dB | ( 20dB |
| Optical Power | 300mW |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

|  |  |  |  |  | I | O |  | I | O |  | I | O |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PMFI |  |  |  |  |  |  |  |  |  |  |  |  |
| Wavelength |  | Grade |  | PM Fiber |  |  | Fiber Length |  |  | Connectors |  |  |
| 1550 | =1 | Premium | =P | Bowtie | =1 | =1 | 1m | =1 | =1 | None | =0 | =0 |
| 1310 | =2 | Grade A | =A | Panda | =2 | =2 | Other | =2 | =2 | FC/PC | =1 | =1 |
| Other | =3 |  |  | Other | =3 | =3 |  |  |  | FC/APC | =2 | =2 |
|  |  |  |  |  |  |  |  |  |  | Other | =3 | =3 |

Polarization Insensitive Fiber Isolator - Single Stage (PIFI-SS)

| Description: The polarization insensitive fiber isolator (PIFI) eliminates back reflection and back scattering of optical signals for any state of polarization. This single stage (SS) version provides high isolation, very low insertion loss, high isolation, high return loss, very low polarization dependent loss, very low polarization mode dispersion, and very high thermal stability in a compact design. |  |  |
| --- | --- | --- |
| Applications: Optical amplifiers (EDFA) CATV fiber optic systems Satellite communications Fiber lasers Optical tests and instrumentation |  | Key Features: High isolation Low loss High thermal stability High return loss Low PDL Low PMD Stable and reliable performance Compact inline package, 5.5mm OD |

Specifications:

|  |  | Single Stage |
| --- | --- | --- |
|  |  | Premium | Grade A |  |
| Center Wavelength (c) |  | 1310, 1550nm |
| Peak Isolation (c, 23°C) | Typ. | ( 42dB | ( 40dB |  |
| Isolation (c±15nm, 23°C, all SOP) | Min. | ( 32dB | ( 30dB |  |
| Insertion Loss (c±20nm, 23°C) | Typ. | 0.4dB | 0.5dB |  |
| Insertion Loss (c±20nm, 0 to 70°C, all SOP) | Max. | (0.5dB | (0.7dB |  |
| Return Loss (Input/Output) | Min. | ( 60/60dB | (55/55dB |  |
| Polarization Dependent Loss (PDL) | Max. | ( 0.05dB | (0.1dB |  |
| Polarization Mode Dispersion (PMD) | Max. | ( 0.2ps | ( 0.25ps |  |
| Optical Power | Max. | 300mW |
| Operating Temperature |  | 0 to 70°C |
| Storage Temperature |  | -40 to 80°C |
| Size |  | Compact inline package, 5.5mm OD |

Ordering Information:

| PIFI-SS |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Grade |  | Fiber Type |  | Fiber Length |  | Connectors |  |
| 1550 | =1 | Premium | =P | SMF28 (250) | =1 | 1m | =1 | None | =0 |
| 1310 | =2 | Grade A | =A | SMF28 (900) | =2 | Other | =2 | FC/PC | =1 |
| Other | =3 |  |  | Other | =3 |  |  | FC/APC | =2 |
|  |  |  |  |  |  |  |  | Other | =3 |

Polarization Insensitive Fiber Isolator - Double Stage (PIFI-DS)

| Description: The polarization insensitive fiber isolator (PIFI) eliminates back reflection and back scattering of optical signals for any state of polarization. This double stage (DS) version provides very high isolation, very low insertion loss, high isolation, high return loss, very low polarization dependent loss, very low polarization mode dispersion, and very high thermal stability in a compact design. |  |  |
| --- | --- | --- |
| Applications: Optical amplifiers (EDFA) CATV fiber optic systems Satellite communications Fiber lasers Optical tests and instrumentation |  | Key Features: High isolation Low loss High thermal stability High return loss Low PDL Low PMD Stable and reliable performance Compact inline package, 5.5mm OD |

Specifications:

|  |  | Double Stage |
| --- | --- | --- |
|  |  | Premium | Grade A |  |
| Center Wavelength (c) |  | 1310, 1550nm |
| Peak Isolation (c, 23°C) | Typ. | ( 58dB | ( 53dB |  |
| Isolation (c±15nm, 23°C, all SOP) | Min. | ( 46dB | ( 44dB |  |
| Insertion Loss (c±20nm, 23°C) | Typ. | 0.5dB | 0.6dB |  |
| Insertion Loss (c±20nm, 0 to 60°C, all SOP) | Max. | (0.7dB | (0.9dB |  |
| Return Loss (Input/Output) | Min. | ( 60/60dB | (55/55dB |  |
| Polarization Dependent Loss (PDL) | Max. | ( 0.05dB | (0.1dB |  |
| Polarization Mode Dispersion (PMD) | Max. | ( 0.05ps | ( 0.1ps |  |
| Optical Power | Max. | 300mW |
| Operating Temperature |  | 0 to 70°C |
| Storage Temperature |  | -40 to 80°C |
| Size |  | Compact inline package, 5.5mm OD |

Ordering Information:

| PIFI-DS |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Grade |  | Fiber Type |  | Fiber Length |  | Connectors |  |
| 1550 | =1 | Premium | =P | SMF28 (250) | =1 | 1m | =1 | None | =0 |
| 1310 | =2 | Grade A | =A | SMF28 (900) | =2 | Other | =2 | FC/PC | =1 |
| Other | =3 |  |  | Other | =3 |  |  | FC/APC | =2 |
|  |  |  |  |  |  |  |  | Other | =3 |

Polarization Maintaining (PM) WDM for EDFA (PMWDM-EDFA)

| Description: The polarization maintaining (PM) WDM for EDFA multiplexes polarized signal with pump and maintains the output signal with high extinction ratio. All signal input and output fibers are polarization maintaining (PM) fibers. It utilizes advanced micro-optic filter technology to yield wideband, low insertion loss, high polarization extinction, high return loss in a compact package. This product can also be used (with minor modification) to multiplex two pump lasers for higher pump power. It can also be provided with a PM isolator integrated in the same package. |  |  |
| --- | --- | --- |
| Applications: Pump/signal WDM for EDFA Multiplexing two pump lasers for higher pump power Sensor systems |  | Key Features: Low loss High extinction ratio High return loss Wide bandwidth High stability and reliability Compact inline package, 5.5mm OD |

Specifications:

| Pump Wavelength | 980nm ((20nm) | 1450-1490nm |
| --- | --- | --- |
| Signal Wavelength | 1550nm (± 20nm) | 1550nm (± 20nm) |
| Insertion Loss (signal) | (0.8dB (0.5dB typical) | (0.8dB (0.5dB typical) |
| Insertion Loss (pump) | (0.8dB (0.5dB typical) | (0.8dB (0.5dB typical) |
| Extinction Ratio | ( 20dB (typ >25dB) |
| Return Loss | ( 50dB (typ>55dB) |
| Directivity | ( 60dB |
| Fiber | PM fiber on 1550nm input port and multiplexed output port, Flexcor on pump port | PM fiber on 1550nm input port and multiplexed output port, SMF28 on pump port |
| Optical Power | 300mW |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

| PMWDM-EDFA |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Signal Wavelength |  | Pump |  | Signal Fiber |  | Pump Fiber |  | Connectors |  |
| 1550 | =1 | 980nm | =1 | Bowtie | =1 | Flexcor | =1 | None | =0 |
| Other | =2 | 1480nm | =2 | Panda | =2 | SMF28 | =2 | FC/PC | =1 |
|  |  | Other | =3 | Other | =3 | Other | =3 | FC/APC | =2 |
|  |  |  |  |  |  |  |  | Other | =3 |

Polarization Maintaining (PM) WDM-1300/1550 (PMWDM-1300/1550)

| Description: The polarization maintaining (PM) WDM multiplexes PM signals (1300/1550) and maintains the output polarization with high extinction ratio using advanced micro-optic filter technology. All input and output fibers are polarization maintaining. It utilizes advanced filter technology to yield wideband, low insertion loss, high polarization extinction, high return loss in a compact package. This product can also be used to multiplex other wavelengths. It can also be provided with a PM isolator integrated in the same package. |  |
| --- | --- |
| Applications: PM signal WDM | Key Features: Low loss High extinction ratio High return loss Wide bandwidth High stability and reliability Compact inline package, 5.5mm OD |

Specifications:

| First Wavelength | 1300nm ((20nm) |
| --- | --- |
| Second Wavelength | 1550nm (± 20nm) |
| Insertion Loss (signal) | (0.8dB (0.5dB typical) |
| Insertion Loss (pump) | (0.8dB (0.5dB typical) |
| Extinction Ratio | ( 20dB (typ >25dB) |
| Return Loss | ( 50dB (typ>55dB) |
| Directivity | ( 60dB |
| Fiber | PM fiber on all ports |
| Optical Power | 300mW |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

| PMWDM-1300/1550 |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength 1 |  | Wavelength 2 |  | PM Fiber |  | Fiber Length |  | Connectors |  |
| 1550 | =1 | 1310nm | =1 | Bowtie | =1 | 1m | =1 | None | =0 |
| Other | =2 | Other | =2 | Panda | =2 | Other | =2 | FC/PC | =1 |
|  |  |  |  | Other | =3 |  |  | FC/APC | =2 |
|  |  |  |  |  |  |  |  | Other | =3 |

Polarization Insensitive WDM for EDFA (PIWDM-EDFA)

| Description: The three port, two wavelength Polarization Insensitive Wavelength Division Multiplexer (PIWDM) combines or separates the optical signal and the pump of EDFAs. It utilizes advanced micro-optic filter technology to yield wide band wavelength flat performance, low loss, polarization insensitive, high isolation performance. This product can also be used (with minor modification) to multiplex two pump lasers for higher pump power. |  |  |
| --- | --- | --- |
| Applications: Pump/signal multiplexing for EDFA Multiplexing two pump lasers for higher pump power Sensor systems Telecommunications, CATV, etc. |  | Key Features: Wide bandwidth, wavelength flat performance, Low loss, High return loss, High channel isolation, Low PDL, High stability and reliability, Compact inline package, 5.5mm OD |

Specifications:

| Pump Wavelength | 980nm ((20nm) | 1450-1490nm |
| --- | --- | --- |
| Signal Wavelength | 1550nm (±30nm) | 1550nm (±30nm) |
| Insertion Loss (signal) | (0.8dB (typ <0.5dB) | (0.8dB (typ <0.5dB) |
| Insertion Loss (pump) | (0.8dB (typ <0.5dB) | (0.8dB (typ <0.5dB) |
| Polarization Dependent Loss | (0.04dB (typ <0.01) |
| Return Loss | ( 50dB (typ >55dB) |
| Directivity | ( 60dB |
| Fiber | Standard: SMF28 on 1550nm input port and multiplexed output port, Flexcor 1060 on pump port. Other combinations available | SMF28 on all ports |
| Optical Power | 300mW |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

| PIWDM-EDFA |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Signal Wavelength |  | Pump |  | Signal Fiber |  | Pump Fiber |  | Connectors |  |
| 1550 | =1 | 980nm | =1 | SMF28 | =1 | Flexcor | =1 | None | =0 |
| Other | =2 | 1480nm | =2 | Other | =2 | SMF28 | =2 | FC/PC | =1 |
|  |  | Other | =3 |  |  | Other | =3 | FC/APC | =2 |
|  |  |  |  |  |  |  |  | Other | =3 |

Polarization Insensitive WDM for 980/1064, 980/1050, 980/1030

| Description: The three port, two wavelength Polarization Insensitive Wavelength Division Multiplexer (PIWDM) for 980/1064, 980/1050, 980/1030 combines or separates the optical signal and the pump of fiber lasers. It utilizes advanced micro-optic filter technology to yield wide band wavelength flat performance, low loss, polarization insensitive, high isolation performance. |  |  |
| --- | --- | --- |
| Applications: Pump/signal multiplexing for 980/1064, 980/1050, 980/1030 fiber lasers Multiplexing two pump lasers for higher pump power |  | Key Features: Low loss, High return loss, High channel isolation, Low PDL, High stability and reliability, Compact inline package, 5.5mm OD |

Specifications:

| Pump Wavelength | 980nm ((20nm) |
| --- | --- |
| Signal Wavelength | 1064(10nm, 1050(10nm, 1040(10nm, 1030(5nm (other wavelengths are available) |
| Insertion Loss (signal) | (1dB (typ 0.5dB) |
| Insertion Loss (pump) | (1dB (typ 0.5dB) |
| Crosstalk as mux (signal in 980 pump port) | (40dB |
| Crosstalk as mux (980 pump in signal port) | (40dB |
| Crosstalk as demux (signal in 980 pump port) | (40dB |
| Crosstalk as demux (980 pump in signal port) | (18dB |
| Polarization Dependent Loss | (0.05dB |
| Return Loss | ( 50dB |
| Directivity | ( 50dB |
| Fiber | Flexcor 1060 on all ports. Other fibers available. |
| Optical Power | 300mW |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

| PIWDM-FL |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Signal Wavelength |  | Pump |  | Signal Fiber |  | Pump Fiber |  | Connectors |  |
| 1064 | =1 | 980nm | =1 | Flexcor | =1 | Flexcor | =1 | None | =0 |
| 1050 | =2 | Other | =2 | Other | =2 | Other | =2 | FC/PC | =1 |
| 1040 | =3 |  |  |  |  |  |  | FC/APC | =2 |
| 1030 | =4 |  |  |  |  |  |  | Other | =3 |
| Other | =5 |  |  |  |  |  |  |  |  |

Integrated Polarization Maintaining Fiber-Optic WDM/Isolator (PMWDM-SPFI/SS)

| Description: The integrated polarization maintaining (PM) fiber-optic WDM/isolator combines the functionality of a PM isolator (1550nm) with a PM-WDM in one compact inline package thus providing significant advantages performance, size, and cost. This integrated hybrid product features high isolation, low insertion loss, high extinction ratio, high return loss, and high thermal stability in a compact design. A range of WDM multiplexing is available. |  |
| --- | --- |
| Applications: EDFA (PM) CATV fiber optic systems External modulator transmitters Fiber lasers Fiber sensors | Key Features: High isolation Low loss High thermal stability High extinction High return loss Compact inline package, 5.5mm OD |

Specifications:

| Pump Wavelength | 980nm ((20nm) | 1450-1490nm |
| --- | --- | --- |
| Signal Wavelength (c) | 1550nm (± 20nm) | 1550nm (± 20nm) |
| Peak Isolation (c, 23°C) | ( 40dB (typ 45dB) | ( 40dB (typ 45dB) |
| Isolation (c, 23°C) | ( 37dB (typ 40dB) | ( 37dB (typ 40dB) |
| Minimum Isolation (c±15nm, 23°C) | ( 30dB (typ >32dB) | ( 30dB (typ >32dB) |
| Insertion Loss (signal) | (1.1dB (0.8dB typical) | (1.1dB (0.8dB typical) |
| Insertion Loss (pump) | (1.1dB (0.8dB typical) | (1.1dB (0.8dB typical) |
| Extinction Ratio | ( 20dB (typ >25dB) |
| Return Loss | ( 50dB (typ>55dB) |
| Directivity | ( 60dB |
| Fiber | PM fiber on 1550nm input port and multiplexed output port, Flexcor on pump port | PM fiber on 1550nm input port and multiplexed output port, SMF28 on pump port |
| Optical Power | 300mW |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

| PMWDM-SPFI/SS |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Signal |  | Pump |  | Signal Fiber |  | Pump Fiber |  | Connectors |  | Isolator |  |
| 1550 | =1 | 980 | =1 | Bowtie | =1 | Flexcor | =1 | None | =0 | Forward | =F |
| Other | =2 | 1480 | =2 | Panda | =2 | SMF28 | =2 | FC/PC | =1 | Backward | =B |
|  |  | Other | =3 | Other | =3 | Other | =3 | FC/APC | =2 |  |  |
|  |  |  |  |  |  |  |  | Other | =3 |  |  |

Polarization Maintaining (PM) Fiber-Optic Circulator (PMFC)

| Description: The three port in-line polarization maintaining (PM) fiber optic circulator routes PM optical signals in a unidirectional sequential order from port 1 to 2 and port 2 to 3 while maintaining the polarization with high extinction ratio. It features low insertion loss, high isolation, high extinction ratio, high return loss and high stability and reliability. The PM circulator is packaged in a small size reliable in-line package compatible with all demanding applications. |  |
| --- | --- |
| Applications: Bi-directional transmission systems WDM & DWDM transmission systems Add/drop multiplexers Fiber optic amplifiers CATV networks Optical test instrumentation | Key Features: Low loss High extinction ratio High isolation High return loss Compact in-line package |

Specifications:

|  | Grade P | Grade A |
| --- | --- | --- |
| Number of Ports | 3 |
| Configuration | 1 to 2, 2 to 3 (all in slow axis) |
| Center Wavelength c | 1550 (±20nm) |
| Insertion Loss (c(20nm, 0-60°C) | (0.8dB (typ 0.5dB) | (1.0dB (typ 0.6dB) |
| Extinction ratio (c(20nm, 23°C) | (20dB (typ 25dB) | (20dB (typ 25dB) |
| Isolation (c(20nm, 23°C, 2-1) | ( 20dB | ( 20dB |
| Isolation (c(20nm, 23°C, 3-2) | ( 20dB | ( 20dB |
| Directivity (1 to 3 or 3 to 1) | ( 50dB | ( 50dB |
| Return Loss | ( 50dB | ( 50dB |
| Optical Power | 300mW (higher power available upon request) |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 80°C |
| Package | Compact inline package, 5.5mm OD |

Ordering Information:

| PMFC-3P |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Grade |  | PM Fiber |  | Fiber Length |  | Cable |  | Connectors |  |
| 1550 | =1 | Premium | =P | Bowtie | =1 | 1m | =1 | None | =0 | None | =0 |
| Other | =2 | Grade A | =A | Panda | =2 | Other | =2 | 3mm | =1 | FC/PC | =1 |
|  |  |  |  | Other | =3 |  |  | 900m | =2 | FC/APC | =2 |
|  |  |  |  |  |  |  |  | Other | =3 | Other | =3 |

Inline Polarization Multiplexer/Divider (PDM-IL-1550)

| Description: The polarization multiplexer/divider (PDM-IL) combines two input signals in orthogonal polarizations into one output. Alternatively it can split the polarization components of an input signal into two PM outputs. This product is designed to provide high extinction ratio with low insertion loss. It features an inline compact package with 5.5mm OD. Various PM fibers can be used at the input ports. The output can be either SMF or PM fiber. PM and SM connectors are available. |  |  |
| --- | --- | --- |
| Applications: Combining or splitting two orthogonally polarized light beams, Passive redundancy switch, Instrumentation, |  | Key Features: Low insertion loss, High optical power, High polarization extinction (as splitter), High return loss, High stability and reliability, Compact inline package. |

Target Specifications:

|  | Premium Grade | A Grade |
| --- | --- | --- |
| Wavelength | 1550nm (±30nm) Other Wavelengths Available |
| Insertion Loss | (0.6dB (typ <0.5dB) | (0.8dB (typ <0.6dB) |
| Return Loss | ( 55dB | ( 50dB |
| Extinction Ratio (as splitter) | (22dB (typ >25dB) | ( 20dB (typ >22dB) |
| Optical Power | 300mW | 300mW |
| Fiber | PM on input ports, SM on output port (PM output optional) |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

|  |  |  |  |  | In Out |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PDM-IL-1550 |  |  |  |  |  |  |  |  |  |  |
| Wavelength |  | Grade |  | Fiber Type |  |  | Length |  | Connectors |  |
| 1550 | =1 | Premium | =P | Bowtie | =1 | =1 | 1m | =1 | None | =0 |
| Other | =2 | Grade A | =A | Panda | =2 | =2 | Other | =2 | FC/PC | =1 |
|  |  |  |  | SMF28 | =4 | =4 |  |  | FC/APC | =2 |
|  |  |  |  | Other | =5 | =5 |  |  | Other | =3 |

Inline Polarization Pump Combiner (PDM-IL-1480)

| Description: The inline polarization pump combiner combines two input 1480nm pumps into one output. This product is designed to handle high optical power with low insertion loss. It features an inline compact package with 5.5mm OD. Various PM fibers can be used at the input ports (Panda, Bowtie, etc.). The output can be either SMF or PM fiber. PM and SM connectors are available. |  |  |
| --- | --- | --- |
| Applications: Combining light from two pump lasers for higher pump power, Combining or splitting two orthogonally polarized light beams, Passive redundancy switch, Instrumentation, |  | Key Features: Low insertion loss, High optical power, High polarization extinction (as splitter), High return loss, High stability and reliability, Compact inline package, 5.5mm OD |

Target Specifications:

|  | Premium Grade | A Grade |
| --- | --- | --- |
| Wavelength | 1400-1500nm |
| Insertion Loss | (0.6dB (typ <0.5dB) | (0.8dB (typ <0.6dB) |
| Return Loss | ( 55dB | ( 50dB |
| Extinction Ratio (as splitter) | (20dB (typ >25dB) | ( 20dB (typ >22dB) |
| Optical Power | 300mW (higher power available upon request) |
| Fiber | PM on input ports, SM on output port (PM output optional) |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

|  |  |  |  |  | In Out |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PDM-IL-1480 |  |  |  |  |  |  |  |  |  |  |
| Wavelength |  | Grade |  | Fiber Type |  |  | Length |  | Connectors |  |
| 1480 | =1 | Premium | =P | Bowtie | =1 | =1 | 1m | =1 | None | =0 |
| Other | =2 | Grade A | =A | Panda | =2 | =2 | Other | =2 | FC/PC | =1 |
|  |  |  |  | SMF28 | =4 | =4 |  |  | FC/APC | =2 |
|  |  |  |  | Other | =5 | =5 |  |  | Other | =3 |

Inline Polarization Pump Combiner (PDM-IL-1060)

| Description: The inline polarization combiner combines two input 1060nm signals into one output. This product is designed to handle high optical power with low insertion loss. It features an inline compact package with 5.5mm OD. Various PM fibers can be used at the input ports. The output can be either SMF or PM fiber. PM and SM connectors are available. |  |  |
| --- | --- | --- |
| Applications: Combining light from two pump lasers for higher pump power, Combining or splitting two orthogonally polarized light beams, Fiber lasers, Passive redundancy switch, Instrumentation, |  | Key Features: Low insertion loss, High optical power, High polarization extinction, High return loss, High stability and reliability, Compact inline package, 5.5mm OD |

Target Specifications:

|  | Premium Grade | A Grade |
| --- | --- | --- |
| Wavelength | 1060(20nm |
| Insertion Loss | (0.8dB (typ <0.5dB) | (1.0dB (typ <0.6dB) |
| Return Loss | ( 50dB | ( 50dB |
| Extinction Ratio (as splitter) | (20dB (typ >25dB) | ( 20dB (typ >22dB) |
| Optical Power | 300mW | 300mW |
| Fiber | PM on input ports, SM on output port (PM output optional) |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

|  |  |  |  |  | In Out |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PDM-IL-1060 |  |  |  |  |  |  |  |  |  |  |
| Wavelength |  | Grade |  | Fiber Type |  |  | Length |  | Connectors |  |
| 1060 | =1 | Premium | =P | Bowtie | =1 | =1 | 1m | =1 | None | =0 |
| Other | =2 | Grade A | =A | Panda | =2 | =2 | Other | =2 | FC/PC | =1 |
|  |  |  |  | Flexcor | =4 | =4 |  |  | FC/APC | =2 |
|  |  |  |  | Other | =5 | =5 |  |  | Other | =3 |

Inline Polarization Pump Combiner (PDM-IL-980)

| Description: The inline polarization pump combiner combines two input 980nm pumps into one output. This product is designed to handle high optical power with low insertion loss. It features an inline compact package with 5.5mm OD. Various PM fibers can be used at the input ports. The output can be either SMF or PM fiber. PM and SM connectors are available. |  |  |
| --- | --- | --- |
| Applications: Combining light from two pump lasers for higher pump power, Combining or splitting two orthogonally polarized light beams, Fiber lasers, Passive redundancy switch, Instrumentation, |  | Key Features: Low insertion loss, High optical power, High polarization extinction, High return loss, High stability and reliability, Compact inline package, 5.5mm OD |

Target Specifications:

|  | Premium Grade | A Grade |
| --- | --- | --- |
| Wavelength | 980(20nm |
| Insertion Loss | (0.8dB (typ <0.5dB) | (1.0dB (typ <0.6dB) |
| Return Loss | ( 50dB | ( 50dB |
| Extinction Ratio (as splitter) | (20dB (typ >25dB) | ( 20dB (typ >22dB) |
| Optical Power | 300mW | 300mW |
| Fiber | PM on input ports, SM on output port (PM output optional) |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

|  |  |  |  |  | In Out |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PDM-IL-980 |  |  |  |  |  |  |  |  |  |  |
| Wavelength |  | Grade |  | Fiber Type |  |  | Length |  | Connectors |  |
| 980 | =1 | Premium | =P | Bowtie | =1 | =1 | 1m | =1 | None | =0 |
| Other | =2 | Grade A | =A | Panda | =2 | =2 | Other | =2 | FC/PC | =1 |
|  |  |  |  | Flexcor | =4 | =4 |  |  | FC/APC | =2 |
|  |  |  |  | Other | =5 | =5 |  |  | Other | =3 |

Inline Fiber Optic Polarizer (FOP)

| Description: The inline fiber optic polarizer offers high extinction ratio, low loss, and high return loss performance over a wideband wavelength range in a compact inline package. Various PM or SM fiber options are available for the input and output ports. |  |  |
| --- | --- | --- |
| Applications: Optical transmission systems EDFA Instruments |  | Key Features: High extinction ratio Low loss High thermal stability High return loss Compact (5.5mm OD) |

Specifications:

|  | P Grade | A Grade | P Grade | A Grade |
| --- | --- | --- | --- | --- |
|  | SM-PM | PM to PM |
| Center Wavelength (c) | 532, 630, 830, 980, 1060, 1310, 1480, 1550, 1620nm Other wavelengths available |
| Bandwidth | (20nm |
| Extinction Ratio (Minimum) | (25dB | (22dB | ( 25dB | ( 22dB |
| Extinction Ratio (Typical) | >30dB | >25dB | >30dB | > 25dB |
| Insertion Loss Max (c±30nm, 23°C) | (0.7dB | (0.8dB | ( 0.8dB | ( 0.9dB |
| Insertion Loss Typical (c±30nm, 23°C) | (0.4dB | (0.5dB | ( 0.5dB | ( 0.6dB |
| Return Loss (Input/Output) | ( 55/55dB | ( 50/50dB | ( 55/55dB | ( 50/50dB |
| Optical Power | 300mW |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

|  |  |  |  |  |  |  | I | O |  | I | O |  | I | O |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FOP |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Wavelength |  | Grade |  | Configuration |  | Fiber |  |  | Length |  |  | Connectors |  |  |
| 1550 | =1 | P | =P | SM-SM | =1 | SMF28 | =1 | =1 | 1m | =1 | =1 | None | =0 | =0 |
| 1480 | =2 | A | =A | SM-PM | =2 | Bowtie | =2 | =2 | Other | =2 | =2 | FC/PC | =1 | =1 |
| 1310 | =3 |  |  | PM-PM | =3 | Panda | =3 | =3 |  |  |  | FC/APC | =2 | =2 |
| Other | =4 |  |  |  |  | Other | =4 | =4 |  |  |  | Other | =3 | =3 |

Faraday Rotator Mirror (FRM)

| Description: The Faraday Rotator (FRM) provides a 90° rotation in the polarization of reflected signals independent of the state of input polarization. This feature eliminates polarization induced fringe fading in interferometers and sensors. It can also provide for forward and backward pass through EDFA for gain optimization. It features low insertion loss and high return loss in a compact package. |  |  |
| --- | --- | --- |
| Applications: EDFA Fiber laser Interferometers Sensors Instrumentation |  | Key Features: Low insertion loss High return loss Precision polarization rotation Compact inline package |

Specifications:

|  | Premium Grade | A Grade |
| --- | --- | --- |
| Wavelength (c) | 1310, 1550nm |
| Spectral width | (20nm |
| Faraday Rotation Angle (c, 23°C) | 45°(0.5° (single pass) 90°(1° (double pass) | 45°(1° (single pass) 90°(2° (double pass) |
| Typical Insertion (Reflection) Loss (c±20nm, 23°C) | ( 0.5dB | ( 0.7dB |
| Maximum Reflection Loss (c±20nm, 23°C) | ( 0.7dB | ( 0.9dB |
| Polarization Sensitivity | 0.02dB | 0.05dB |
| Return Loss | ( 30dB | ( 25dB |
| Optical Power | 300mW |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package |

Ordering Information:

| FRM |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Grade |  | Fiber Type |  | Fiber Length |  | Connectors |  |
| 1550 | =1 | Premium | =P | SMF28 (900) | =1 | 1m | =1 | None | =0 |
| 1310 | =2 | Grade A | =A | SMF28 (250) | =2 | Other | =2 | FC/PC | =1 |
| Other | =3 |  |  | Other | =3 |  |  | FC/APC | =2 |
|  |  |  |  |  |  |  |  | Other | =3 |

Polarization Maintaining (PM) Faraday Rotator (PMFR)

| Description: The Polarization Maintaining (PM) Faraday Rotator (PMFR) provides a 45° rotation in either transmission direction. The input and output fibers are PM fibers aligned so that the output fiber major axis are at 45° from the input fiber. Therefore in one direction, transmission will be maintained along the same axes (slow ( slow or fast ( fast). In the opposite direction, the axes will be switched. It features very low insertion loss, high extinction ratio, and high return loss. In a compact package. |  |  |
| --- | --- | --- |
| Applications: CATV fiber optic systems External modulator transmitters Fiber lasers Fiber gyros |  | Key Features: Very low loss Very high thermal stability High extinction High return loss Compact inline package, 5.5mm OD |

Specifications:

|  | Premium Grade | A Grade |
| --- | --- | --- |
| Center Wavelength (c) | 1310, 1480, 1550nm (other wavelengths available) |
| Spectral Width | (20nm |
| Typical Insertion Loss (c±10nm, 23°C) | 0.5dB | 0.6dB |
| Maximum Insertion Loss (c±10nm, 23°C) | ( 0.6dB | ( 0.8dB |
| Extinction Ratio (PM fiber output) | ( 22dB | ( 20dB |
| Return Loss | ( 60/55dB | ( 55/50dB |
| Faraday Rotation Angle (c,23°C) | 45°(1° | 45°(2° |
| Optical Power | 300mW |
| Operating Temperature | 0 to 70°C |
| Storage Temperature | -40 to 85°C |
| Size | Compact inline package, 5.5mm OD |

Ordering Information:

| PMFR |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Grade |  | Fiber Type |  | Fiber Length |  | Connectors |  |
| 1550 | =1 | Premium | =P | Bowtie | =1 | 1m | =1 | None | =0 |
| 1310 | =2 | Grade A | =A | Panda | =2 | Other | =2 | FC/PC | =1 |
| Other | =3 |  |  | Other | =3 |  |  | FC/APC | =2 |
|  |  |  |  |  |  |  |  | Other | =3 |

Polarization Maintaining Jumper (PM Patch-Cord (PM Jumper), PMJ)

| Description: The polarization maintaining (PM) jumper (PM patch cord) is a PM connectorized polarization maintaining PM fiber. It can be supplied cabled in 3mm cable, 900m tight buffer or loose tube, or bare fiber with 400m coating. It features high extinction ratio as a result of very accurate active alignment between PM major axis and the connector key. Various PM fibers and connectors are available. |  |  |
| --- | --- | --- |
| Applications: Communications CATV Instrumentation Sensor systems |  | Key Features: Active alignment High polarization extinction ratio PM misalignment ((2( Low loss High return loss High stability and reliability |

Specifications:

| Grade | Premium Grade | A-Grade |
| --- | --- | --- |
| Wavelength | 830, 980, 1060, 1310, 1480, 1550nm (Other wavelengths Available) |
| Insertion Loss | (0.5dB (typical 0.2dB) | (0.5dB (typical 0.2dB) |
| Polarization Extinction Ratio | (25dB (typ >30dB) | ( 23dB (typ >25dB) |
| PM misalignment | (2( | (3( |
| PM Fiber Available | Panda, Bowtie, etc. |
| Cable | Options: 3mm, 900m tight buffer, 900m loose tube (Bare fiber 400m is also available) |
| Connectors | FC/APC, FC/PC, FC/SPC, FC/UPC, SC/APC, SC/PC, etc. |

Ordering Information:

| PMJ |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Wavelength |  | Grade |  | Fiber Type |  | Cable |  | Fiber Length |  | Connectors |  |
| 1550 | =1 | Premium | =P | Bowtie | =1 | 3mm | =1 | 1m | =1 | None | =0 |
| 1480 | =2 | Grade A | =A | Panda | =2 | 900 | =2 | Other | =2 | FC/PC | =1 |
| 1310 | =3 |  |  | Other | =3 | 400 | =3 |  |  | FC/APC | =2 |
| Other | =4 |  |  |  |  | Other | =4 |  |  | Other | =3 |